## Slide 1: A Monocular Visual Odometry Experiment Using ORB-SLAM Library
Farhad Mirkazemi
“Any sufficiently advanced technology is indistinguishable from magic”
Arthur C. Clarke

## Slide 2: Monocular Visual Odometry
The Act of Determining Moving Target Position and Attitude Using Single Camera Image Sequences
Unique Only Up to A Scale Factor

## Slide 3: General Algorithm
Capture Images as Input:
Determine Camera Intrinsics and Lens Distortion Parameters

## Slide 4
LensDistortion
Radial distortion occurs when light rays bend more near the edges of a lens than they do at its optical center
xdistorted = x(1 + k1*r2 + k2*r4 + k3*r6)
ydistorted= y(1 + k1*r2 + k2*r4 + k3*r6)
Tangential distortion occurs when the lens and the image plane are not parallel
xdistorted = x + (2 * p1 * x * y + p2 * (r2 + 2 * x2))
ydistorted = y + (p1 * (r2 + 2 *y2) + 2 * p2 * x * y)

## Slide 5: Matlab Camera Calibration Algorithm
Solve for the intrinsics and extrinsics in closed form, assuming that lens distortion is zero
Estimate parameters simultaneously, including the distortion coefficients, using nonlinear least-squares minimization (Levenberg–Marquardt algorithm) setting the initial estimate of the intrinsics and extrinsics to the preceding step and the distortion coefficients to zero

## Slide 7
My Iphone 6 Camera Parameters | 
Parameter | Estimated Value
Image Sizex | 1920
Image Sizex | 1080
fx | 1890.1946
fy | 1887.7924
px | 934.0193
py | 524.4038
k1 | -0.0935
k2 | 0.5849
k3 | 00376
p1 | -0.0030
p2 | -0.0029

## Slide 8: General Algorithm
Use Feature-Based Algorithm to Detect Points of Interest on Consecutive Images
ORB_SLAM uses ORB Features which are oriented multi-scale FAST (oFAST)corners with a 256 bits descriptor associated

## Slide 9: ORB Keypoints
FAST and its variants are the method of choice for finding keypoints in real-time systems that match visual features.
It is efficient and finds reasonable corner keypoints, although it must be augmented by a Harris corner filter to reject edges and provide a reasonable score.
Many keypoint detectors include an orientation operator (SIFT and SURF are two prominent examples), but FAST does not.

## Slide 10: FAST: Features from Accelerated Segment Test
A segment test criterion operates by considering a circle of Sixteen,(ORB uses 9) pixels around the corner candidate p
The original detector classifies p as a corner if there exists a set of n contiguous pixels in the circle which are all brighter than the intensity of the candidate pixel plus a threshold t, or all darker than − t
Further Machine Learning Algorithm process to ensure higher speed for lower size of the circle

## Slide 11: FAST

## Slide 12: Harris Filter Augmentation
For a target number N of keypoints, we first set the threshold low enough to get more than N keypoints, then order them according to the Harris measure, and pick the top N points
FAST does not produce multi-scale features. ORB employs a scale pyramid of the image(8 scale), and produce FAST features (filtered by Harris) at each level in the pyramid
Reminder
Compute spatial derivatives ,
Construct structure tensor M:
Harris Response Calculation
Finding the local maxima within the 3 by 3 window

## Slide 13: ORB Corner Orientation
ORB uses a simple but effective measure of corner orientation, the intensity centroid
Find moments of a patch:
Find centroid:
Construct a vector from the corner’s center, O, to the centroid, OC .
Orientation of the Patch is:

## Slide 14: ORB Descriptor
BRIEF: Binary Robust Independent Elementary Feature
Consider the binary test:
The feature is defined as a vector of n-binary test:
rBRIEF: To be invariant to in-plane rotation
ORB discretizes the angle to increments of 2π/30 (12 degrees), and construct a lookup table of precomputed BRIEF patterns. As long as the keypoint orientation θ is consistent across views, the correct set of points Sθ will be used to compute its descriptor.

## Slide 16: Initialization
Find Initial Correspondences
Parallel Computation of Homography and Fundamental Matrix
Normalized DLT
8-point in Each Iteration RANSAC

## Slide 17: Initialization
Structure From Motion Recovery
Full Bundle Adjustment
If the Scene is Planar
Choose H
If not
Choose F
)=

## Slide 18: ORB Tracking
Tracking using motion-only Bundle adjustment as below, having all points in local area is fixed and only the camera pose is to be optimized

## Slide 19: ORB Tracking
If tracking was successful for last frame, the algorithm uses a constant velocity motion model to predict the camera pose and perform a guided search of the map points observed in the last frame.
If not enough matches were found, it uses a wider search of the map points around their position in the last frame. The pose is then optimized with the found correspondences

## Slide 20: Results

## Slide 21: Results

## Slide 22: Results

## Slide 24: References
[1] R. Mur-Artal, J. M. M. Montiel, and J. D. Tardos, “ORB-SLAM: a ´ versatile and accurate monocular SLAM system,” IEEE Trans. Robot., vol. 31, no. 5, pp. 1147–1163, 2015.
[2] E. Rublee, V. Rabaud, K. Konolige, and G. Bradski, “ORB: an efficient alternative to SIFT or SURF,” in IEEE International Conference on Computer Vision (ICCV), Barcelona, Spain, November 2011, pp. 2564– 2571

## Slide 25
Questions?